## Slide 1: 3.2 Logic Gates and Logic Circuits
Use the following logic gate symbols:
NOT AND OR
NAND NOR XOR
Understand and define the functions of :
NOT, AND, OR, NAND, NOR and XOR (EOR) gates
Construct the truth table for each of the logic gates above
Construct a logic circuit
Construct a truth table
Construct a logic expression
Notes and guidance

## Slide 2: Today
Everything on syllabus
Understand: What is a logic gate
Able: Draw truth tables
Answer: Which gate has only 1 input

## Slide 3: 1.3.1 – Logic Gates
Use Logic Gates to create electronic circuits
Understand and define logic gates
AND
OR
NOT
NAND
NOR
XOR
EOR
Truth Tables

## Slide 4: Today
Understand : What are logic gates
Able : Identify logic gates
Answer : How many inputs does NOT have

## Slide 5: What is a logic gate?
Why do computers use binary?
Because electricity can be either on or off, 1 or 0
But you must control the flow of electricity
You use logic gates to SHOW how you will control the flow of electricity
You’ll do this in Physics also.

## Slide 6: 6 types
AND
OR
NOT
NAND
NOR
XOR (sometimes called EOR)

## Slide 7: AND
Two inputs
One output
Input 1 AND Input 2 must be on for Output to be ON
Written as A . B = Output
Input A | Input B | Output
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 8: OR
Two inputs
One output
Input 1 OR Input 2 must be on for Output to be ON
Written as A + B = Output
(yes I know using + is stupid for OR)
Input A | Input B | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 9: NOT
ONE inputs
One output
If Input in OFF then output is ON
If Input is ON then output is OFF
Written as Ā
Input A | Output
0 | 1
1 | 0

## Slide 10: Quick Quiz
Name 2 logic gates
Name 2 more
And 2 more please
Why do we use logic gates?
Which gate has two inputs?
Which gate has one input
What does + mean?
Which gate needs to have input 1 and Input 2 on for output to be on?
Which gate has one output?
Which gate is simply the opposite of the input?
What are the names of the table?

## Slide 11: NAND
Stands for NOT AND
Two Inputs
One Output
Output is ON unless both inputs are ON
Written as A . B = Output
Input A | Input B | Output
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 12: NOR
Stands for NOT OR
Two Inputs
One Output
If any Input is ON then output is OFF
Written as A + B = Output
Input A | Input B | Output
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 13: XOR or EOR
Stands for Exclusive OR
Two Inputs
One Output
If the Inputs are the same then then output is OFF
Written as A B
Input A | Input B | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 26: From the exam paper
Draw the logic circuit and truth table for:

## Slide 28: Logic circuit and truth table

## Slide 29: Answer

## Slide 30: Logic circuit and truth table

## Slide 31: Answer

## Slide 32: Truth table for:

## Slide 33: Answer

## Slide 34: Test Others
https://academo.org/demos/logic-gate-simulator/
Draw a logic circuit
Make it complicated
Swap places with another student
The other student must write a truth table for YOUR circuit