## Slide 1: 4.1 Central Processing Unit (CPU) Architecture
Show understanding of the basic Von Neumann model for a computer system and the stored program concept
Show understanding of the purpose and role of registers, including the difference between general purpose and special purpose registers
Show understanding of the purpose and roles of the Arithmetic and Logic Unit (ALU), Control Unit (CU) and system clock, Immediate Access Store (IAS)
Show understanding of how data are transferred between various components of the computer system using the address bus, data bus and control bus
Show understanding of how factors contribute to the performance of the computer system
Understand how different ports provide connection to peripheral devices
Describe the stages of the Fetch-Execute (F-E) cycle
Show understanding of the purpose of interrupts

## Slide 2: Today
Show understanding of the basic Von Neumann model for a computer system and the stored program concept
Show understanding of the purpose and role of registers, including the difference between general purpose and special purpose registers
Show understanding of the purpose and roles of the Arithmetic and Logic Unit (ALU), Control Unit (CU) and system clock, Immediate Access Store (IAS)
Show understanding of how data are transferred between various components of the computer system using the address bus, data bus and control bus
Understand: What makes up the Von Neumann model
Able: Know each Buses role
Answer: Why we use the Von Neumann model

## Slide 3: Von Neumann Architecture
The Von Neumann architecture is called that because a man called John Von Neumann decided that the way computers worked were stupid and he had a better idea.
John Von Neumann came up with this idea in 1945.
Before this you had one computer to run a program but you needed another computer to hold all the information.
Imagine if you had one laptop to make PPTs but every time you needed to save information or get information you need to use another laptop.
John Von Neumann thought it would be better if you can store your program AND your data in one machine.
It became the Von Neumann architecture or sometimes called the Stored Program architecture.
Its still used now!

## Slide 4: Von Neumann architecture
Von Neumann architecture only has 3 main parts. But each of these main parts have parts inside them.
The three main parts are:
1. Processor
2. Memory
3. Input/Output

## Slide 5: 3 parts
Here are the main parts.
Even this is a little confusing. It has 3 parts but is input / output 1 part or 2??
Its treated as 1 part for now. Later it will become 2.
You will notice that the Processor can connect with Memory and Input / Output.
The memory does not connect with input / output
PROCESSOR
MEMORY
INPUT / OUTPUT

## Slide 6: System Bus
See those black lines that connect the processor, memory and IO
That is the System Bus.
Its called a Bus because it transport data
Its called the System Bus because it the main bus of the whole system.
The System Bus is actually 3 different buses.
1: Address Bus
2: Data Bus
3: Control Bus
PROCESSOR
MEMORY
INPUT / OUTPUT

## Slide 7: 1: Address Bus (Yellow line)
When the processor needs to read or write to memory it uses the address bus to specify the physical address.
PROCESSOR
MEMORY
INPUT / OUTPUT

## Slide 8: 2: Data Bus (Red line)
The address bus carries where you want to read or write your data,
The data bus is used to carry the actual data
The processor can go to memory.
The memory can go to processor
The processor can go to IO
The IO can go to processor
Its bi-directional
PROCESSOR
MEMORY
INPUT / OUTPUT

## Slide 9: 3: Control Bus (Blue line)
The control bus carries control signals.
It says if the processor is reading or writing from the memory or IO
We need the control bus because otherwise there maybe data on the data bus that is trying to read and write at the same time. So the control bus is used to make sure of the timing of the other buses
The processor can go to memory.
The memory can go to processor
The processor can go to IO
The IO can go to processor
Its bi-directional
PROCESSOR
MEMORY
INPUT / OUTPUT

## Slide 10: System Bus
3 different buses
1: Address Bus
Processor says the physical address it wants to use
2: Data Bus
Data is sent or received on this
3: Control Bus
Used to make sure timing is good and tells other parts what the processor is doing

## Slide 11: Three Letters
OMG!! Computer Science loves 3 letters. WTF?
The Processor can also be called the CPU – Central Processing Unit.
The Memory can also be called RAM - Random Access Memory
RAM is volatile memory, this means when you switch off the computer the data inside in the RAM is gone.
Inside the processor and inside the memory are other parts. Get ready…. 

## Slide 12: All the parts we will learn about:
ALU – Arithmetic Logic Unit
CU – Control Unit
System Clock
IAS - Immediate Access Store
PC – Program Counter
MAR – Memory Address Register
MDR – Memory Data Register
ACC – Accumulator
IX – Index Register
CIR – Current Instruction Register
SR – Status Register

## Slide 13: Registers
Q. What’s RAM?
A. Random Access Memory.
Q. Is it volatile?
A. Yep. Turn power off and your data in the RAM goes away.
Q. Can you hold one thing in the RAM or many things?
Many things
Q. Is it fast?
A. Yep, its fast because its primary memory
Q. What’s a register?
A. It’s the name for another type of memory. Its small, it can only hold one thing at a time. But its really fast, usually because it lives INSIDE the CPU.

## Slide 14: Inside the CPU – The ALU
So inside the CPU is something called the ALU – Arithmetic Logic Unit.
The job of the ALU is to do all the math calculations.
It does Addition, Subtraction, AND, OR, NOT, NAND, NOR, XOR
CPU
ALU

## Slide 15: Inside the ALU - ACC
Inside the ALU is a register.
A register is a small piece of memory that holds something
The register inside the ALU is so important that it gets a special name.
The Accumulator. ACC
The ALU does all the math operations, the ACC holds the answer from these operations
In many books and websites, it will show the ACC outside of the ALU, this is done just for ease, in real life the ACC is inside the ALU.
CPU
ALU
ACC

## Slide 16: Inside the CPU – MAR
Another register inside the CPU is the MAR. Memory Address Register.
Can RAM hold one thing or many things?
Many.
So when you want something from RAM, you have to say WHERE in RAM you want to go to. You have to say the location of the data you want. You have to say the address.
The address you want to go to is stored in the MAR.
It uses the address bus
CPU
ALU
ACC
MAR

## Slide 17: Inside the CPU – MDR
So the MAR stores the address via the address bus.
The MDR – Memory Data Register, stores the actual data.
It uses the data bus
**This bit not in syllabus**
You also have another register called the MBR – Memory Buffer Register.
In real life, the data goes to the MBR and then goes MDR.
CPU
ALU
ACC
MAR
MDR

## Slide 18: Inside the CPU – MAR and MDR
There are two things you can do.
Read something from RAM
Write something to RAM
If you want to read from memory then you must:
1: The address of the location is put in the MAR
2: The physical place in memory is enabled for a read
3: The value is put in the MDR
To write to memory:
1: The address is put in the MAR
2: The data is put in the MDR
3: A write enable signal is given
4: The value from MDR is put where it needs to be (which is the address in MAR)
CPU
ALU
ACC
MAR
MDR

## Slide 19: Inside the CPU - IX
We said the MAR holds the memory address. This is true.
But there is also something called the IX – Index Register
The Index Register is used if we use Index Addressing Modes
What is Index Addressing Mode?
Lets say you start from memory location 3
Then the next piece of data is 8,
Then the next is 13
Then the next is 18….23…..28…..33…..38…..43
What’s the pattern?
It started at 3 and goes up every 5
CPU
ALU
ACC
MAR
MDR
IX

## Slide 20: Inside the CPU – IX – Index Register
So the IX is actually two things:
The Source Index, SI and the Destination Index, DI.
The source index, SI, is also called the base index. This is where we start from.
Then we have our index
Then we have the Destination Index, DI
Our example 3…8…13…18….23….28…33…38…..43…..48……..
The SI (or base) is 3
Our index is 5
The DI is just our SI + Index
But for Cambridge all we need to know is:
Index Register (IX) is the value we use to find out the next address to go in the MAR

## Slide 21: Inside the CPU - CU
Q. What are the three buses in Von Neumann? A. Address Bus, Data Bus and Control Bus
Q. The address bus connects to what?
MAR
Q. The data bus connects to what?
MDR
Q. What about the control bus?
A. The control bus connects to the Control Unit (CU)

## Slide 22: Inside the CPU - CU
The control unit manages what everything else in the CPU does. It controls the CPU.
It doesn’t do any of the work, that’s still done by the ALU.
But it tells the ALU what to do
Inside the Control Unit there are some more registers:
PC – Program Counter CIR – Current instruction Register SR – Status Register
CPU
ALU
ACC
MAR
MDR
IX
Control Unit

## Slide 23: Inside the Control Unit – PC - Program Counter
The Program Counter, PC.
It says what is the next thing we will do.
So if we have a list:
0. Sit down
Stand up
Spin around
Stop spinning
Jump up and down
Die
Our first instruction is always 0. So our PC will be 0 and we will sit down.
While we are sitting down, our PC will point to the next instruction, 1 Stand up.
Once 0-Sit down is finished, we look at our PC and it tells us we must do ‘1’ which is stand up. While we are doing 1-stand up, the PC gets ready and says 2.
In real life its not 0, 1, 2…. But the memory location of the next instruction so the PC has a memory location that then goes into the MAR
CPU
ALU
ACC
MAR
MDR
IX
Control Unit
PC
CIR
SR

## Slide 24: Inside the Control Unit – CIR – Current Instruction Register
The Current Instruction Register, CIR, is sometimes called the IR Instruction register.
The PC points to the thing we will do next. The CIR says the thing we are doing right now.
So, our PC starts at 0 (sit down)
Then we sit down
Because we are doing this currently, we put 0 in the Current Instruction Register (CIR) so now our CIR says 0 and our PC points to the next instruction
PC = Says what to do next
CIR = Says what we are doing right now
CPU
ALU
ACC
MAR
MDR
IX
Control Unit
PC
CIR
SR

## Slide 25: Inside the Control Unit – SR – Status Register
The status register is also called the flag register
It holds INFORMATION about the result, not the actual result
It does two things with the information about the result
Checks for conditions
Places flags
CPU
ALU
ACC
MAR
MDR
IX
Control Unit
PC
CIR
SR

## Slide 26: Status Register
There are 8 conditions that it checks for:
I : Global Interrupt
T : Copy Storage
H : Half Carry
S : Sign
V : Two’s Compliment Overflow Flag
N : Negative flag
Z : Zero flag
C : Carry Flag
I | T | H | S | V | N | Z | C

## Slide 27: Status Register
I : Global Interrupt
If you want to have interrupts you set this to 1
T : Copy Storage
If you want one bit to be copied
H : Half Carry
If you have a half-carry operation (more on this in Year 13)
S : Sign
Says if the result is not a simple integer
V : Two’s Compliment Overflow Flag
If you have overflow after two’s complement
N : Negative flag
Says if the result is a negative number
Z : Zero flag
Says if the result is a zero
C : Carry Flag
Says if we need to carry a bit

## Slide 28: Status Register
So if our status register looks like this:
It will mean:
I = 1 = We will allow interrupts
T = 0 = Nothing to copy
H = 0 = Its not half-carry
S = 1 = It is not a normal integer
V = 0 = Its not two complement overflow
N = 1 = It is a negative number
Z = 0 = Its not zero
C = 1 = We will need to carry
We don’t actually know what math function we did or what the answer is, but we know INFORMATION about the answer. That’s what the Status Register does
I | T | H | S | V | N | Z | C
1 | 0 | 0 | 1 | 0 | 1 | 0 | 1

## Slide 29: Status Register - Flags
So now you have information about the result, what to do with it?
Sometimes you don’t want to do anything. But sometimes you want to.
The times you want to do something you place a flag.
A flag is a stupid word that means ”if this is true” do this….
So if we want to say, if the result is a zero, then interrupt the program and quit everything. Then we use a flag for our ‘Z’ bit in our status register.

## Slide 30: Immediate Access Store IAS
We have done:
MAR
MDR
MBR
CIR
PC
SR
ACC
IX
And for some unknown reason, Cambridge wants us to do Immediate Access Store – IAS.
The IAS is the place where you hold all the data that you are currently using.
It’s a group name for our registers

## Slide 31: Group Names
We said the IAS is the group name for the registers we know because it holds all the data we are currently using.
But there are two other terms we must know:
Special Purpose Registers
General Purpose Registers
Special purpose registers is what we have done. These are registers that have a definitive purpose and role
General purpose registers are registers that programs can use just to hold something that they need for later. They have no fixed role other than this.

## Slide 32: So we have:
A processor (CPU) with ALU, MAR, MDR and a CU and IX.
The CU has a PC, CIR and SR
And we have a System Bus which is made up from an Address Bus, Data Bus and Control Bus which links the CPU to Memory and IO
MEMORY
INPUT / OUTPUT
CPU
ALU
ACC
MAR
MDR
IX
Control Unit
PC
CIR
SR

## Slide 33: Today
5. Show understanding of how factors contribute to the performance of the computer system
Understand: What impacts a computer’s speed
Able: Explain how and why these factors impact the speed
Answer: What can I do to make my computer faster

## Slide 34: Computer Speed
We know what parts are inside a CPU
But how fast is it?
There are a few things that impact a computer’s speed
Clock Speed
Bus Width
Cache Memory
Processor type and cores

## Slide 35: System Clock / Clock Speed / CPU Clock
Okay we know what all of the parts in a CPU does.
How quickly do they do it?
Well this is timed by the System Clock.
The system clock is also called the CPU clock
It’s a tiny quartz crystal on your motherboard that sends out a pulse.
Each pulse is counted.
The number of pulses you have is equal to your system clock
Its measured in Hertz (Hz) per second
So if your clock is 1Hz, 1 Hertz, it means it does 1 pulse per second
1MHz, 1 Megahertz means 1 million things per second
1GHz, 1 Gigahertz means 1 billion things per second.

## Slide 36: So that’s it right….
So that’s it right…. If my Clock Speed is 3 GHz, it means my processor can do 3 billions things per second, it means that’s how fast my computer is…right???
Nope.
Remember how the MAR uses the address bus, the MDR uses Data bus and Control Unit uses the control bus.
Well what if my CPU is super super fast, but my bus is slow?

## Slide 37: Bus Speed and Width
Your bus has two measurements:
Bus Speed
Bus Width
Bus Speed is measured in Hertz.
Its how fast the bus can do something per second.
Modern computers have bus speeds measured in at least 1 MHz – 1 million things per second.
Bus width
The bus is just a wire (or usually printed on a motherboard)
Bus width is how many physical wires are connected.
If there are 16 wires connected then your bus width is 16. If 32 wires then your bus width is 32.
If your bus width is 32, it means that you can send 32 bits of data at the same time (parallel)

## Slide 38: Cache Memory
This is a form of DRAM – Dynamic RAM
But its much smaller and much faster.
Q. Why is it faster? A. Its closer to the CPU, sometimes built inside the CPU. It also uses its own dedicated bus.
Cache memory has 3 levels. Each level describes how physically close the cache memory is to the CPU
Level 1 (L1 Cache) - Fastest. Built inside the CPU. Small capacity. Sometimes called Primary cache
Level 2 (L2 Cache) – Fast. Can be built in CPU or sometimes built on a separate chip. Has its own bus so it doesn’t slow down even if the system bus is slow. Has more capacity then L1 cache. Sometimes called secondary cache
Level 3 (L3 cache) – This type of cache is faster than standard RAM but it used to help L1 and L2 cache to hold data. It can pass data to L1 and L2 quicker than RAM.
So the more L1, L2 and L3 cache you have the more you can store in this faster type of memory and the fact it uses its own bus also means it won’t slow down even if everything else does.

## Slide 39: Processor Type and Cores (and threads)
In the past, the speed of your CPU was just measured by the system clock.
So 3GHz meant that your processor can do 3 billions things per second.
But, its still only one thing a time, it just does those things so fast that it can do 3 billion of them in a second.
But still only one at a time.
So then, CPU manufactures found a better way.
Have one physical CPU chip, but split it so it behaves like two. This is dual core.
If you have quad core, then its one CPU chip but behaves like 4 (quad) CPU’s because it has 4 physical parts to it, its just 4 parts on one chip. It means it can do 4 things at the same time.
So you can decide, is it better to have single core at 3GHz or quad core at 2GHz?

## Slide 40: Processor Cores
Okay, so if quad core is like having 4 CPU’s because you can do 4 things at once…. Why not just actually have 4 physical CPU’s?
Requires more cooling
Requires more power
Requires a bigger socket / more sockets on the motherboard
One CPU split into 4 can communicate quicker then 4 individual CPU’s
Having more cores is cheaper then having more CPU’s

## Slide 41: Processor Threads
This bit is not in your syllabus but useful.
Intel did something before making multi-core processors. They created something called “Hyperthreading”
It sounds the same as multicore.
You have one physical CPU chip but this CPU is hyperthreaded into two threads. So your Operating system will think its two CPU’s. But its not real, you don’t have two cores, you have single core, but it just lies to your OS and says “hey, I’m multicore” But Intel was not allowed to say multicore, because it wasn’t, so they used the term hyperthreading.
Now you get multicore and hyperthreading on the same chip.
So a quad core 16 thread CPU has one chip, with 4 cores and 16 virtual threads

## Slide 42: Today
6. Understand how different ports provide connection to peripheral devices
Understand: How different ports connect to a computer
Able: Explain the power delivery of each port
Answer: Why we have different ports?

## Slide 43: Von Neumann
There was 3 parts (or 4 or 5 parts) to Von Neumann, what were they?
Processor
Memory
Input / Output
You could say:
Processor
Memory
Input
Output
System Bus
We’ve done Processor and we did memory. Now time for input / output

## Slide 44: Honestly:
Cambridge added this for no real reason.
They want us to learn about 3 ports but no real logic behind it, but its in syllabus so we must do.
We will do:
VGA
HDMI
USB

## Slide 45: VGA
VGA = Video Graphics Array
Uses screws to keep the cable in place
Has 15 pins (usually)
Can send video signals / picture signals
Is only used now because some old hardware still uses it
Old
Cheap
Analogue
Degrades over long length

## Slide 46: But how does VGA work?
Remember your display is made of red, green and blue.
VGA uses 15 pins
Your computer monitor can use up to 4 bits to describe itself. Each bit can refer to a pin
Pin | What it does
1 | Outputs Red
2 | Outputs Green
3 | Outputs Blue
4 | Colour Monitor or Mono Monitor (ID2)
5 | Ground / Earth
6 | Red Ground
7 | Green Ground
8 | Blue Ground
9 | Voltage +-5V
10 | Synchronize Grounds
11 | Colour Monitor or Mono Monitor (ID0)
12 | Same as pin 11 but for different types of monitor. (ID1)
13 | Horizontal Sync (HSYNC)
14 | Vertical Sync (VSYNC)
15 | Monitor bit 3 (ID3)

## Slide 47: VGA Pinout
Pin | What it does
1 | Outputs Red
2 | Outputs Green
3 | Outputs Blue
4 | Colour Monitor or Mono Monitor (ID2)
5 | Ground / Earth
6 | Red Ground
7 | Green Ground
8 | Blue Ground
9 | Voltage +-5V
10 | Synchronize Grounds
11 | Another monitor bit (ID0)
12 | Another monitor bit (ID1)
13 | Horizontal Sync (HSYNC)
14 | Vertical Sync (VSYNC)
15 | Another monitor bit (ID3)

## Slide 48: HDMI
HDMI = High Definition Multimedia Interface
Newer
Digital
Video / Pictures and sound
Three variants: Full; Mini and Micro
Because its digital it makes no difference what material the cable is made from. But people still try to sell Gold HDMI for better conductivity because Gold VGA cables did make a *very small* difference

## Slide 49: HDMI Pinout
Uses 19 pins and there is NO WAY that Cambridge will ask about these pins.

## Slide 50: USB
USB = Universal Serial Bus
Very common
Digital
Can transfer power and data
At least 4 pins.
2 pins are for power
1 pin for data in
1 pin for data out
Digital
Many variants

## Slide 51: Today
7. Describe the stages of the Fetch-Execute (F-E) cycle
Understand: What is the Fetch Execute Cycle
Able: Use register notation to describe the fetch execute cycle
Answer: What does [ ] mean in RTN?

## Slide 52: Fetch Decode Execute Cycle
We know the different parts of a computer
We even know what factors affect the computer’s speed
We even know, way too much about the input and outputs.
But how does a processor actually process data.
This is described as the Fetch Decode Execute Cycle. FEDC
Sometimes its called the Fetch Execute Cycle. FEC or FE Cycle

## Slide 53: Video Questions
What is the order of the FE Cycle?
Is data from RAM read top to bottom?
Instead of Assembly, what language will it be in real life?

## Slide 55: Task
Here are the stages. What is the correct order?
PC has address of next instruction
PC copies to MAR
Lookup MAR and put data in the MDR
Copy from MDR to CIR
PC points to the next instruction
Instruction is decoded and executed
Repeat

## Slide 56: Task
Correct order
PC has address of next instruction
PC copies to MAR
Lookup MAR and put data in the MDR
Copy from MDR to CIR
PC points to the next instruction
Instruction is decoded and executed
Repeat
Step | Fetch execute cycle steps | Simplified description
1 | The PC contains the address of the memory location that has the next instruction which has to be fetched | PC has address of next instruction
2 | This address is then copied from the PC to the MAR via the address bus | PC copied to the MAR
3 | The contents (instruction) at the memory location (address) contained in MAR are then copied into the MDR | Lookup MAR and get contents. Copy contents into the MDR
4 | The contents (instruction) in the MDR is then copied and placed into the CIR | Copy MDR contents into the CIR
5 | The value in the PC is then incremented by 1 so that it now points to the next instruction which has to be fetched | PC is then incremented by 1
6 | The instruction is finally decoded and then executed by sending out signals (via control bus) to the various components of the computer | The instruction is decoded and then executed
7 | Repeat | 

## Slide 57: Fetch (Get)
The PC copies the address of the next instruction to the MAR.
The memory looks at the address its been told to and puts data the MBR
The CPU copies the data from the MDR to the CIR (All of this is fetch)
The PC is incremented so the next command is ready to go

## Slide 58: Decode
So we got an instruction that is loaded…but now we need to understand it. We need to decode it.
The decode process allows the CU to decide what instruction should be performed. The ALU actually does the work but the CU controls the ALU
This is done by an Instruction Decoder (ID)
An instruction is actually two different things joined together. The Job of the ID is to understand these parts.
The two parts are:
Opcode
Operands
Opcode = Operation Code. Says what should be done with the data. Like ADD (for add) or SUB (for subtract) or MOV (for move)
Operand = Is data that you wish to process. The data can be a memory address which holds data.
Example:
LOAD A,
LOAD is the Opcode
A s the Operand

## Slide 59: Execute
So we have the instruction LOAD A
But A is a memory location 10. So its like saying LOAD whatever is in memory location 10.
So we now need to execute this instruction. To execute LOAD 10. So we need to get whatever is in memory location 10…..what do we call it when we get something…
Fetch
So the fetch things happens again. The MAR is told address 10. The data that is in location 10 is put into the MDR. Then the content in the MDR is placed in the ACC so we can use it later
The PC is already pointing to the next address, so that gets copied into the MAR. Then the data is taken from memory and put in the MDR…and the whole thing happens again. The next video will show us how to LOAD data, ADD data and STORE data. Its just going to add up two numbers – but we need to LOAD, ADD and STORE.

## Slide 60: Register Transfer Notation
This is real pointless, but Cambridge want it.
You should understand the order of the FEC.
But Cambridge want you to write it in a special way using Register Transfer Notation – RTN
But its simple enough to understand:
If something is in square brackets, [ ] , then it means we take the value from it.
Batman  [Amar] So here we are giving Batman the value from Amar

## Slide 61: Task
Put in the correct order. Note that because we are using REGISTER transfer Notation, we only care about the REGISTERS. THIS IS NOT THE FULL FETCH EXECUTE CYCLE but only the REGISTERS
MAR  [PC]
MDR  [Memory]
CIR  [MDR]
PC  [PC] + 1
[CIR] Decode and Execute

## Slide 62: Answers
Note that because we are using REGISTER transfer Notation, we only care about the REGISTERS. THIS IS NOT THE FULL FETCH EXECUTE CYCLE but only the REGISTERS
MAR  [PC]
MDR  [Memory]
CIR  [MDR]
PC  [PC] + 1
[CIR] Decode and Execute

## Slide 63: Today
8. Show understanding of the purpose of interrupts
Understand: What is an interrupt?
Able: Describe why we need them
Answer: How does the ISR handle them?

## Slide 64: Interrupts
Okay, you know Von Neumann, you know what affects the speed and you even know FEC.
Last thing….
What happens if your computer is busy doing the FEC but you want it to stop and do something more important instead? Can it??
Yes, of course. This is called an interrupt
Interrupt = When you stop FEC to do something more important

## Slide 65: What are the causes?
We said interrupts are when something more important needs to happen. But what are these somethings?
Hardware interrupts
This is when a signal from hardware is given to interrupt the current process.
An example is if you press the Escape key when running code or the Mute key when listening to audio
2. Software interrupts
This is when software decides there is to be an interrupt. There are two main types of software interrupt
  Normal Interrupt
  This is when an instruction in the code says there should be an interrupt
  Exception
  This is when the interrupt is unplanned and an error happened.

## Slide 66: Some more
Timer Interrupts
Always happens at a certain time. Example to refresh your display screen
Input/Output interrupts
Most common, you press a key on the keyboard, it sends a signal to the CPU, the CPU stops what it’s doing and does what you pressed then returns to what it was doing before.

## Slide 67: More registers
Okay so an interrupt just happened…..what actually occurs?
Well first we need to know another register inside the CPU
The Interrupt Register (IR)
Most of the time this register will be all 0’s to signal that there is no interrupt
Software | Hardware | IO | Timed
0 | 0 | 0 | 0

## Slide 68: Interrupt Register
But now lets say you pressed a key on your keyboard, Escape, to trigger an interrupt. Your IR now looks like:
At the next FE Cycle, the CPU checks the IR (Interrupt register) it sees there has been a hardware interrupt because there’s a 1 and now it will process the interrupt.
The way the interrupts are handled are done by the Interrupt Service Handling Routine (ISR)
Software | Hardware | IO | Timed
0 | 1 | 0 | 0

## Slide 69: Interrupt Service Handling Routine - ISR
The ISR is actually a control line dedicated for interrupts
The program counter is pointing to the next instruction as normal.
An interrupt happens
Now the program counter must stop pointing to what would have happened as normal and now it will point to the first instruction stored in the ISR
The address of the instruction in the ISR is moved to another register, like the MAR but its not the MAR, its just a different register
The CPU performs the instructions until the interrupt has been handled.
While it’s doing this, the PC will point back to what it would be pointing to if the interrupt didn’t happen.

## Slide 70: Little more complicated then that
Okay your interrupt happened. The Interrupt register changed value to it shows it.
On the next cycle the CPU can see that the IR changed and now the PC will point to the first instruction in the ISR
But….we need to interrupt the interrupt. Once the CPU has recognised an interrupt happened and will deal with it, it must also send another signal to say “Hey, I saw you want an interrupt, I will handle it, stop sending me interrupt requests”
So there is a delay between the interrupt signal being received and the start of actually dealing with the interrupt. This is called Interrupt Latency

## Slide 71: But what about my stored data?
So when an interrupt happens, you already have data in your IX, PC, MAR, MBR, MDR, ACC. What happens to these?
Either two things will happen.
All of the contents of those registers get stored somewhere else, and when the interrupt finishes then it gets replaced
You start from the beginning again / wherever the PC left off